## Slide 1: Liquid Separation Technologies
COMPANY INTRODUCTION · 2026
Process design, engineering and original equipment for water treatment and industrial purification.

## Slide 2: What we will cover
CONTENTS
01 Pilot Setup
02 Colour Breakthrough
03 Performance
04 Regeneration

## Slide 3: Process Design & Engineering
SECTION
02

## Slide 4: Capability overview
Ion exchange — column design, resin selection and regeneration modelling.
Membranes — RO, NF and UF process packages built to duty.
Adsorption — regenerable adsorbent systems with no brine stream.
One takeaway per slide — replace this line with the point the audience must remember.

## Slide 5
PILOT RESULTS
80%
COLOUR REDUCTION
0
BRINE WASTEWATER
2.4
BED VOLUMES / HOUR

## Slide 6: Two-stage decolorisation — design basis
TECHNICAL APPENDIX · A2
Parameter | Stage 1 | Stage 2 | Unit
Resin volume | 25 | 25 | L
Flow rate | 60 | 60 | L/h
Feed colour | 1,245 | 480 | IU
Outlet colour | 480 | 35 | IU
Removal | 61 | 93 | %
Chart: 
| Cycle 1 | Cycle 2 | Cycle 3
Total removal | 81 | 80 | 79
Two stages in series are required to reach <35 IU; a single stage cannot meet spec.

## Slide 7: Let's design the process.